9.04 – Notes
ETR113

Voltage: Potential difference in charge between two points
Current: Rate of flow of electrons in a single instance
Resistance: Material resistance to current

Ohm’s Law: The relationship between these elements

Volts = V
Amperes (Amps) = I
Resistance (Ohms) = Ω

V = I cdot R

Solve for I:

V = I cdot R newline newline 5 = I cdot 220 newline newline {V} over {R} = I newline newline {5} over {220} = ? newline newline I = .0227 A newline newline I = 22.7 mA

Series Circuit: Voltage Divider

Parallel Circuit: Current Divider

Properties of Series Circuits:

Total Resistance = All resistances added together

R_{T} = R_{1} + R_{2}

Resistor Value of LED: Find values on datasheet

({V_{S}} - {V_{F}}) over {I_{F}}