9.11 – Notes
ETR113

Parallel Circuit: Current Divider

Properties of Parallel Circuits:

Parallel circuits have multiple paths for current to flow.

Voltage is the same for each path.

The Sum of each current path is equal to the total current:

I_{T} = I_{1} + I_{2} ... + ... I_{N}

If a path is broken, the other paths still flow...

Total Resistance = NOT - All resistances added together

R_{T} = {R_{1} * R_{2}} over {R_{1} + R_{2}}

OR

{1} over {R_{T}} = {1} over {R_{1}} + {1} over {R_{2}} ... + ... {1} over {R_{N}}

Which is the same as:

R_{ T} = 1 over { {1} over {R_{1}} + {1} over {R_{2}} ... + ... {1} over {R_{N}} }